## Slide 1
Notes: Hello everyone, and a very warm welcome to “Unveiling ProtaStructure 2027.” This is the very first time we're showing these new features in public, and honestly, we couldn't be more excited to share them with you. We're confident this release is going to make a real difference for our users — so let's jump right in.

## Slide 2
Mustafa Tümer Tan
Partner & Consultant
Structural Engineer, MSc
Altuğ Güler
CTO
Structural Engineer, MSc
Jaime Sempere
Regional Channel Manager
Notes: Before we get into the new features, just a quick hello from the team. Today we will be presenting together with Mustafa and our regional channel manager Jaime.

## Slide 3: Major Focus of ProtaStructure 2027
1
Key Highlights
2
Performance Improvements
3
Enhanced Design Documentation
4
Modeling and Visualization
5
RC Detailing
6
The New ProtaSteel
Notes: Here's where we're headed today. We'll walk through six themes together: the headline highlights, the performance gains, the enhanced design documentation, the modeling and visualization upgrades, the RC detailing improvements, and the brand-new ProtaSteel. Every one of these came straight from your feedback, and they all point at the same goal — making your everyday workflows faster and more reliable.

## Slide 4
Under the Spotlight:
Key Highlights
Notes: So let's put that first set of features under the spotlight — here are the highlights everyone's been waiting for.

## Slide 5: Key Highlights
Cold Form Design to AISI S100 and EN1993
Notes: Let's start with one of the big ones in ProtaStructure 2027 — full cold-formed steel design according to American and European Codes.
You can model, analyze, and design your cold-formed members without ever switching over to a separate specialist tool.
Here you can see that it is actually the same familiar design workflow that is already in-place for hot-rolled steel members. But of course there are key differences from hot-rolled design. Member capacity is determined by the Direct Strength Method. In this method strengths are computed directly from elastic buckling loads of the gross cross-section for each buckling mode. Distortional buckling is treated as a standalone limit state.
The implementation covers tension checks, compression checks including global flexural, flexural-torsional, torsional, local buckling, and distortional buckling. Also major and minor axes bending checks, shear checks, combined actions, and serviceability deflection.
Supported section shapes include open profiles like C, channel shapes, Z shapes and hat shapes. Also closed profiles like Rectangular Hollow Sections, Square Hollow Sections and circular pipes.

## Slide 6: Key Highlights
Centralized & Improved Report System
Notes: Next, we rebuilt the Report system from the ground up, all around a single Report Submission Set. You add reports from the Repository, drag to reorder them, and produce one merged file — no more jumping in and out of individual design menus.
ProtaStructure even builds a default set based on your model and flags anything that's missing.
You can brand your reports with a logo, date, and QR code, drop in the new cover page and Model Information report, and see every error and warning at a glance.

## Slide 7: Key Highlights
Spiral Staircase Modeling and Design
Notes: Here's one of our most-requested additions: spiral staircases. You can now model, analyze, and design them. You simply show the origin and a diameter distance as a reference. Then you can place the actual spiral staircase around this reference by setting it at the left, at the right or at the center of it.
You can adjust the total turning angle and reverse the climbing direction. You can even view the rebars in 3D.
Then just like all the rest of the physical members spiral stairs, can be copied to the other storeys.
The analytical model is generated automatically. Spiral staircases can be supported from the inner edge, the flight ends, or both depending on how the physical model is produced. If there is a column at the inner edge the inner nodes are connected to the top of this column.

## Slide 8: Key Highlights
ETABS Model Import & Improved Export
Notes: We've also built a true two-way bridge with ETABS. Import brings the full model across — geometry, grids, materials, sections, slabs, walls, loads, and combinations — with units handled automatically. And we actually rebuilt Export from scratch too. The new export produces a high-fidelity e2k file that keeps your bracing, mass sources, diaphragms, and 3D geometry intact, all the way from ETABS v13 to v23. So no more manual remodeling on either side.

## Slide 9: Key Highlights
Indian Seismic Code IS1893-2025
Notes: For our colleagues working on Indian projects, we've updated IS 1893 to the 2025 edition. You get the new hazard maps, spectral parameters, and design provisions right out of the box — no manual adjustments needed.

## Slide 10: Key Highlights
Shearwall Boundary Element Checks to ACI318
Notes: Figuring out whether a shearwall needs a special boundary element used to be a manual exercise.
Not anymore — ProtaStructure 2027 runs both the ACI displacement-based and stress-based checks at the same time and reports the outcome directly in the RC Shearwall Design report. No extra spreadsheets required.

## Slide 11: Key Highlights
Floor Torsion: Check at Selected Columns
Notes: You can now choose which columns drive the floor torsion check, direction by direction. This is really handy on irregular plates where the worst case isn't sitting at the corners. And the columns you select show up in the report, so the whole check stays fully traceable.

## Slide 12: Key Highlights
Pushover Target Displacement – NSR10 (Colombia)
Notes: Another seismic enhancement here,
Target Displacement Calculation for Pushover Analysis is now available for the Colombian Seismic Code, NSR-10. So if you're working on Colombian projects, you can run a complete nonlinear static pushover analysis with code-compliant target displacement.

## Slide 13: Key Highlights
RC Beam & Column Design to Thailand DPT1302-61
Notes: We've extended RC Beam and Column design to cover the DPT clauses over ACI.
The fully integrated clauses include longitudinal reinforcement limits, column dimension checks, plastic hinge length, confinement zone spacing, mid-span spacing, and the shear design logic.
So engineers on Thai projects get fully code-compliant beam and column designs inside ProtaStructure.

## Slide 14: Key Highlights
Footing Stability Checks
Notes: We've added overturning and sliding stability checks to pad footing design. The Factor of Safety limits are determined automatically, based on your selected design code and load combination type — static or seismic and wind. Stability checks cover American-based Standarts, Indian Standarts, Turkish Standards, Eurocode and British Standarts. The critical Factor of Safety values across all combinations show up in the design summary, and there's a detailed matrix table in the report.

## Slide 15: Key Highlights
Multiple Links in Wide Beams
Notes: ProtaStructure 2027 now supports up to seven links for wide beam design. You set the minimum width limits, and the algorithm follows them incrementally. So it picks the right number of links automatically. There's also a new link pattern for wide beam layout, giving you extra flexibility to meet your detailing requirements.

## Slide 16
Performance Improvements
Notes: Now let's talk about something you feel every single day — performance.

## Slide 17: Performance Improvements
4x Analysis Speed
Notes: Now let’s talk about performance improvements and here's a big one.
We've comprehensively re-engineered the analysis engine, and it delivers a 4-fold speed improvement across every model size. If you're working on large, complex multi-storey structures, you'll see dramatically shorter run times — which means faster design iterations and a much more productive workflow.

## Slide 18: Performance Improvements
5x Faster Analysis Result Processing
Notes: Contour map generation for very large models requires processing of thousand of nodes. Now this analysis post-process has been boosted up to 5-fold. This improves F.E. Foundation Report generation performance particularly if contour maps are requested to be included in the report.

## Slide 19: Performance Improvements
Very Large Models with Similar Storeys
Notes: And the performance story doesn't stop there. Small-size models are always easy to manipulate even there are similar storeys that act together. However as the model gets bigger and bigger, the manipulation of the model becomes harder. We have revised the connectivity algorithm to perform up to 200 fold better depending on the size of the model when editing members. That means far easier manipulation for very large models.

## Slide 20: Performance Improvements
10x Faster Report Engine
Notes: ProtaStructure 2027 also moves to a PDF-based report generation engine. This one change tackles those slow report times in large models — reports now generate up to 10-fold faster. And it's not just about speed: the new engine gives you more visually appealing reports and a better quality print preview. Even large, content-heavy design reports get prepared and rendered in seconds.

## Slide 21
Design Documentation Enhancements
Notes: So what about the enhancements in design documentations? Let's take a look.

## Slide 22: Design Documentation Enhancements
New Slab Detailed Report
Notes: There's a brand-new, comprehensive slab design report. It includes strip profile images with deflection, shear, and moment values; detailed bending design and deflection check calculations, complete with formulas and code clause references; and moment and steel bar area contours for the finite element strips in flat slab systems.

## Slide 23: Design Documentation Enhancements
Cover Page and Model Info Report
Notes: Here's another one you asked for a lot. Using the new Report Center, you can now add a neat cover page and a model information report — with 3D and plan views — right into your combined report.

## Slide 24: Design Documentation Enhancements
Improved Post Analysis Checks
Notes: We've enhanced the post-analysis report to communicate the behaviour factor and eccentricity calculations far more clearly — that’s available for all seismic codes including American, Colombian and Eurocode. You now get much cleaner traceability, straight from your input parameters through to code-compliance verification.

## Slide 25: Design Documentation Enhancements
Truss Sketch in Steel Design Report
Notes: Truss diagrams now appear directly in your truss design reports, with the utilization ratios highlighted in color codes — so you can read the results at a glance.

## Slide 26: Design Documentation Enhancements
Improved Quantity Takeoff Reports
Notes: Concrete and Formwork Quantity Reports can now be filtered by storey, and all quantity reports export to Excel. Steel member quantities are broken down by member type. Now retrofit walls, column jackets, and piles each get their own separate columns in the quantity tables.

## Slide 27: Design Documentation Enhancements
Extended Excel Export Coverage
Notes: We've rolled out Export to Excel across a whole range of reports. That now includes Analysis Results, Base Reactions, Column and Wall Design Forces, Beam and Column Rebar Tables, and the Concrete, Formwork, Steel, Sheeting, and Shear Stud Quantity Tables.

## Slide 28
Modeling and Visualization
Notes: Let's shift gears now and look at modeling and visualization.

## Slide 29: Modeling and Visualization
Member Selection Grouping
Notes: You can now create named selection groups and assign any combination of members to them. On large models, this is a huge time-saver — it dramatically speeds up amendments, verification, and change management. You can add or remove members on-the-go or you can use the group editor for a broader perspective. It’s also possible to assign a key combination for quick selection of group members.

## Slide 30: Modeling and Visualization
Wind Columns
Notes: We've added a Wind Column option to steel columns. When you designate a member as a wind column, it's designed only for vertical and wind loads — seismic forces are excluded. That lets you accurately design secondary structural elements that aren't part of the lateral force-resisting system.

## Slide 31: Modeling and Visualization
Staircase Load Copying and Nonorthogonal Landings
Notes: We don't always work with nice orthogonal plan layouts — sometimes you need to fit a staircase into a non-orthogonal region. ProtaStructure 2027 lets you do exactly that. No matter how the insertion region is shaped, you can safely model a staircase in it and take it all the way through analysis, design, and detailing. ………
And you can now copy staircase loads to other staircases, which really cuts down repetitive data entry when a project has lots of stair configurations. You see that the shape does not matter here.

## Slide 32: Modeling and Visualization
Drawing Primitives – Move & Copy
Notes: You can now copy and move primitive drawing entities right in the modelling environment. So you don’t need to repeat drawing them manually. These primitive entities help you create custom shaped columns, custom shaped slabs, slab holes and drops. They also form a custom layout for staircases.

## Slide 33: Modeling and Visualization
Composite Slabs – Batch Edit
Notes: And you can now edit multiple composite slabs at the same time, straight from the Member Table.

## Slide 34: Modeling and Visualization
Analysis Results Report - Search
Notes: We have added a search box in the Analysis Result dialog. So you can go directly to the member you want to report

## Slide 35: Modeling and Visualization
Analysis Results Report - Search
Notes: Steel bar optimization window is now modeless. That means you can switch between columns while the windows stays open.
Well there are more productivity improvements that we could not mention here. You can find them on the new features document.
That’s all from me today. Thank you very much for your attention. Now I am handing over to Mustafa for further news from 2027 version…

## Slide 36
Automated & Interactive RC Detail Drawings
Notes: Now let's move into RC detailing — where things get both automated and interactive.
We have listened to our users an done a lot of work in RC detailing which you will find very useful.

## Slide 37: RC Detailing
Lap Cranks in Columns
Notes: This was one of the top requested features which contributes to quality and accuracy of the detailing.
There's a new option that applies cranks to column elevation rebar laps. This is a detailing practice that's commonly required in Europe and India, where lapped bars at floor levels need to show the crank geometry explicitly in the elevation drawing.

## Slide 38: RC Detailing
Confinement Along Beam and Column Splices
Notes: Confinement reinforcement along beam and column splice regions is now detailed automatically, in line with the applicable code requirements. T
hat makes sure the correct transverse reinforcement ends up in your splice zones — for US Code and South American projects.

## Slide 39: RC Detailing
Similar Column Detail Grouping
Notes: Similar columns and walls within a storey can now be shown together in a single elevation detail, which saves a lot of paper space. And the important part is — the quantity take-off automatically accounts for the grouping.

## Slide 40: RC Detailing
Basement Wall Detailing – Merging and Adjacent Columns
Notes: Basement wall elevations can now be drawn alongside their connected column elevations, and merged along the axis.

## Slide 41: RC Detailing
Shearwall Elevations with Side View
Notes: We've also added a side view of the shear wall elevations as a detailing option.

## Slide 42: RC Detailing
Basement Wall Containment Options
Notes: And there are now separate containment settings for basement walls, so the detailing lines up correctly for those merged wall-and-column details at basement level.

## Slide 43: RC Detailing
Full Anchorage Length for Beam Bottom Bar
Notes: Bottom bar anchorage options are now available for cases where bob length is greater than beam depth.

## Slide 44: Key Highlights
Punching Reinforcement Detailing
Notes: ProtaStructure can take into account the effect of punching reinforcement during the punching checks.
2027 version also highlights reporting and detailing enhancements for punching reinforcement.
Users now have better control over the quantity of the punching reinforcement. Full detail drawing generation is available in ProtaDetails. All three types of punching reinforcement can be drawn and included in the quantity take off.

## Slide 45: RC Detailing
Formwork Scaffolds Quantity Take Off
Notes: ProtaStructure already supports a comprehensive design and visualization for formwork scaffolds.
With the new version, ProtaDetails now includes a dedicated take-off command for these components.
You just select a region on the drawing that contains your formwork applications and details, and a cumulative quantity take-off table is generated automatically.

## Slide 46
Steel Connection Design, Detailing and Fabrication
Notes: I hope you liked what you saw in ProtaDetails side of things. Now, as for ProtaSteel, our team worked hard to bring important improvements and the new features to life. Let’s see what we are up to.

## Slide 47: ProtaSteel
Handrail Post Connection Types
Notes: A brand-new dedicated connection macro has been introduced specifically for Type 4 handrail post configurations.
This macro will make your life easier by enabling rapid, standardized modelling of industrial walkways, platforms, and stair detailing.

## Slide 48: ProtaSteel
New Macro: Purlin and Girt Flush Connections
Notes: In some scenarios, it may be necessary to place the purlins and girts flush with the supporting member face or within the main member.
And for these kind of cases, ProtaSteel offers a new connection type where you can connect the purlin or the girt using a bolted plate directly welded to the main member.

## Slide 49: ProtaSteel
New Macro: Hollow Section End Plate Connection
Notes: It is also quite common to use hollow sections due to their versatility and availability. A new macro has now been introduced so that the hollow sections can now be connected automatically with an end plate. And just like every other macro, these macro can be customized to suit your requirements.

## Slide 50: ProtaSteel
New Macro: End-Plate Splice Connection for Curved Beam
Notes: With the new ProtaSteel, End Plate splice supports curved members

## Slide 51: ProtaSteel
New Drawing Module with UNDO Functionality
Notes: With ProtaSteel 2027, you can put together your general arrangement, part, and assembly drawings far more efficiently. Once you've wrapped up the clash assessment and numbering, your model is ready for fabrication and shop drawings — and ProtaSteel's dedicated drawing module makes that whole process even easier. We've recently enhanced the module's ribbon toolbar and given the user experience a big lift together with the UNDO function, so it's simpler than ever to create general arrangement drawings, drop in annotations and dimensions, and inspect your part and assembly drawings.

## Slide 52: ProtaSteel
Assembly and Part Drawing Improvements
Notes: Let's talk about enhanced drawing control and detailing. ProtaSteel 2027 brings some significant enhancements that give you far greater control over your drawing content and presentation. For a start, you can now customize assembly and part drawings on a per-sheet basis. New view and section override options let detailers decide exactly which views and cross-sections get generated, so you end up with cleaner, more focused fabrication drawings. On top of that, there's single-part view rotation, advanced dimensioning and annotation options, multi-leg welding symbols, and intelligent filtering tools — all improving drawing quality, readability, and detailing flexibility. ProtaSteel 2027 also delivers several workflow enhancements to boost your productivity across the whole drawing lifecycle. Any manual views, sections, and callouts you add to automatic drawings are now preserved when those drawings update, so you're not redoing work. And with support for opening multiple drawings side by side, improved viewport-based clipping, and the new “Ready to be Issued” status, reviews, coordination, and approvals all become a lot smoother — which means faster, more efficient drawing production.

## Slide 53: ProtaSteel
Export Connections to IdeaStatica (with Internal Forces)
Notes: Now, ProtaSteel already gives you detailed design reports for the most commonly used connections — but on some projects, analyzing complicated or user-defined steel connections with Component-Based Finite Element Analysis is simply unavoidable. At Prota, we believe in open collaboration, so we build links between our products and industry-leading software. Our latest addition is the IDEA StatiCa FEA Links. You can export your automatic or user-defined connections to IDEA StatiCa and carry on from there whenever you need to. All you do is start the IDEA StatiCa Checkbot inside ProtaSteel and select your primary members and connection components, just following the wizard. We introduced this IDEA StatiCa export in the previous version, and it got fantastic feedback — so this time we've taken it further. You can now export the internal forces acting on the connections to IDEA StatiCa in a tabular format; an Excel file is generated automatically, listing the internal forces needed for the connection FE analysis for each relevant load combination. And those forces are the post-processed results, according to your selected design and seismic codes.

## Slide 54
Notes: Thank you so much for being here today! We've covered a lot of ground — and there's still more to come. So before we wrap up, let me leave you with some exciting news.

## Slide 55: Prota Help Center
Learning Hub & Technical Support
Notes: Once you become a ProtaStructure client, you get a lot more than just software. As a ProtaStructure subscriber, you get first-class technical support, regular updates and enhancements to your software, and full access to the Prota Help Center. Inside the Help Center, you can browse knowledge base articles, join the community forums, submit and track your support tickets, and get the help you need — fast.

## Slide 56: New Website
A Fully Redesigned Website
Notes: Also, We're really excited to introduce our brand-new website, launching soon — redesigned from the ground up to give you a faster, cleaner, and more intuitive experience. And this isn't just a visual refresh; it's a smarter, richer resource, built with you in mind.

## Slide 57: Smarter Knowledge Base
Everything You Need, Easier to Find — Smarter Knowledge Base
Notes: But that's not all. We've also significantly expanded our Knowledge Base which will be available on our website.
Whether you're after technical documentation, tutorials, step-by-step guides, or best practices, everything you need is now far easier to find.

## Slide 58
Notes: And before we close — let's stay connected! We're active on LinkedIn, Facebook, YouTube, and Instagram, where we regularly share product updates, industry insights, technical tips, and a behind-the-scenes look at what we're working on. If you want to be the first to hear about new features, upcoming events, and exclusive content, give us a follow — it only takes a second, and you'll always be in the loop. Just search for Prota Software on any of these platforms; we'd love to have you in our community.

## Slide 59
Notes: And that brings us to the end of our presentation today. We really hope you enjoyed what you saw. As you can tell, ProtaStructure 2027 is packed with new features — far too many to cover in a short session — so we're putting together detailed documents and presentations to walk you through them all. Stay tuned for our upcoming events on the new version. Thank you all so much for joining us, and we hope to see you next time.